## Slide 1: NETWORK TRAFFIC CONTROLLING SYSTEM
Team: SVSH
Supadma Kadabi
Vibhashree Hippargi
Sachin Kumar
Hamida Aliveya

## Slide 2: What and How?
SMART? - When the components of a traffic control system, for example, traffic signals and autonomous vehicles can interact with each other about the situations and take decisions without the need for human intervention, we can term them ‘Smart’.
HOW? - With the help of cellular V2X (C-V2X) or dedicated short-range communication (DSRC). This allows vehicles to ‘see through the eyes’ of their traffic fellows and significantly extend the sensing range provided by their own sensors, such as cameras, radar, or lidar.

## Slide 3: V2X:
V2X sends around 10messages/second
Messages contain important parameters viz. accurate geographical location, the actual speed, velocity and direction of the vehicle, and the status of brakes and hazard warning lights.
For building Smart infrastructure, VS2X RSU (Road Side units) are used. They have their own processing power, send and receive messages.
Several elements of traditional road elements can be linked to RSUs
By this, buses and urban maintenance fleets can request priority at V2X-enabled intersections.
E.g.: In Denver, Colorado, snowplow trucks cross intersections by requesting a green light, causing less disruption to traffic.

## Slide 4
Reference: Commsignia

## Slide 5: Block Diagram

## Slide 6: Internal Block diagram

## Slide 7: Constraints and Parametric Diagrams
Notes: Constraint diagram - A constraint block is a special kind of block used to define equations so that they can be reused and interconnected. Constraint blocks have two main features: a set of parameters and an expression that constrains those parameters.
Parametric – To define the relationship bw the constraint parameters
Fuel in tank = tank capacity * odm marking/total number of odometer lines

## Slide 8: Accident Occurred scenario

## Slide 9: State Machine
Use case : Accident Occurred

## Slide 10: Code for the state machine:
** Current state = Driving_Normal
A : Distance from message transmitter <=50m
B: Accident Occurred ?
C: Alternate Path available ?
A | B | C | State change
T | T | T | Decelerate -> Changed Path -> Driving Normal
T | T | F | Decelerate -> Changed lane direction -> Driving Normal
T | F | T | Driving Normal
T | F | F | Driving Normal
F | T | T | Driving Normal
F | T | F | Driving Normal
F | F | T | Driving Normal
F | F | F | Driving Normal

## Slide 11: Code Walkthrough
Classes: Vehicle and Accident_Scenario States: driving_normal, decelerating, changed_path, changed_lane_direction Accident_Scenario: distance_from_message_transmitter, accident_occurred, alternate_path_available State Transition: Condition Check in Switch Case

## Slide 12: Tinker Cad
Let us see the states in Action!
Ultrasonic distance sensor to check distance
Push button to set if accident occurred or not
Push button to set if alternate path(exit) is available or not
LED – accident occurred
LED – alternate path available
Driving_Normal
Decelerate
Changed Path
Changed Lane direction
Arduino

## Slide 13: Scheduling
EDF (Earliest Deadline First)
Schedulable iff U <=1
RM (Rate Monotonic)
Schedulable iff U <= n(
Where,
U =

## Slide 14: Tasks are as follows
 | Accident Occurred (AO) | Emergency Vehicle approaching (EV) | Pedestrian Hotspot ahead (PH)
Ci (Execution time) | 1 | 2 | 3
Ti (Period) | 4 | 6 | 8
Di(deadline) | 4 | 6 | 8
Tasks
Time in ms
U = 1/4 + 2/6 + 3/8 = 0.95

## Slide 15: P_RM
Missed deadline!
U (0.95) NOT <=0.77. Hence it is NOT safe to schedule in RM.
From the image, we can clearly see that Task 3 i.e. Pedestrian Hotspot ahead has missed the deadline. In Hard-RTOS, it would cause severe impacts.

## Slide 16: P_EDF
U (0.95) is <=1.
Hence it can be scheduled
in EDF.
From the image, we can see
That, no task has missed
its deadline

## Slide 17: Inspection Time!
Inspection, in any field, plays a significant factor in the success of a product. During this phase, potential errors could be identified, and the shortcomings can be overcome in a new release. It also saves the project time and money caused by late detection of bugs.
Below listed are the original and improved versions that lead to our final documents:
1. State Machine code has been improved
2. Diagrams have been improved
3. Test cases were reviewed before the execution
4. Push buttons were added to Tinker Cad

## Slide 18: Testing
Tool: Visual Studio 2022
Framework: Gtest
Coding Language: C++
Test scenarios: Positive test, negative test, interface test

## Slide 19: Test Cases
Test Scenarios
Unit Tests
Check whether there's an accident
Defect Tests
Check if vehicle accepts negative input
Interface Tests
Check whether there's an alternative path
Check if system accepts negative distance
Vehicle change speed or path according to corresponding state

## Slide 20: Test case output
POSITIVE TESTS
NEGATIVE TESTS

## Slide 21: Test case output
INTERFACE TESTS